## Slide 1: Automated Honey Extractor
Group 3
Dmytro Boichev
Petr Boychev
Kira Farney
Brandon Parmeter

## Slide 2: Motivation
Beekeeping equipment, honey extractors in particular are very expensive.
Current lower-end beekeeping machinery (under $1500) is severely lacking in terms of performance.
The honey extraction process is too time consuming compared to other beekeeping duties.

## Slide 3: Current Extractor Used
Current Extractor
  Tangential Design
  Frame Capacity: 2
  Hand Operated
  Stainless Steel

## Slide 4: Goals and Objectives
Design and build a high performance automated honey extractor.
Extract honey with minimal input from the user.
Optimize and decrease time consumption of the honey extraction process.
Achieve the previous goal in under $1000.

## Slide 5: Specifications
Component | Design Specification
Frame Holder | The extractor supports up to 15 frames.
Vat | The extractor has a vat capacity of 20 Gallons.
Heating System | The heating system maintains a vat temperature of 43 degrees Celsius.
Motor | The motor is capable of spinning the frame holder up to 250 RPM.
Wireless Connectivity | The extractor can be operated wirelessly from a distance of 30 feet.

## Slide 6: Mechanical Characteristics
Vat
  Gauge 16 Grade 304 stainless steel with a bottom made of Gauge 13
  Diameter: 32 inches
  Height: 31inches
  Total Volume: 24931.68 Cubic Inches (108 Gallons)
  Usable Volume: 4608 Cubic Inches (20 Gallons)

## Slide 7: Frame Holder
Frame Holder
  Radial Design
  Grade 304 stainless steel
  Radius: 13.5’’
  Height: 31’’
  Frame Capacity: 15
  Shaft Diameter: 5/8’’

## Slide 8: Block Diagram

## Slide 9: Heating System

## Slide 10: Heating System
The heating system speeds up the extraction process by decreasing honey viscosity.
Micro Controller
Temperature
Sensor
Heating Coil
Heating Coil Driver

## Slide 11: Heating Element
Flexible Silicone-Rubber Heating Sheet
  Adhesive backed for easy installation
  1” x 30” strip
  115V @ 1.3 Amps x 3
  Can be heated up to 149 oC
  150 x 3 Watt power capabilities

## Slide 12: Sensors

## Slide 13: Temperature Sensor
An infrared temperature sensor provides feedback information to the heating system.
MLX90614
Temp range: -40°C ~ 125°C
Communicates via I2C interface
Voltage: 4.5 V ~ 5.5 V
Accuracy: ±1°C

## Slide 14: Humidity Sensor
Water content of the honey is affected by the humidity level during extraction.
High water content negatively affects the quality of the honey (leads to fermentation).
HIH-4030-003
Humidity Range: 0 ~ 100% RH
Operating Temp: -40°C ~ 85°C
Accuracy: ± 3.5% RH

## Slide 15
Motor Controller

## Slide 16: Motor Controller
Required motor output: ½ HP
AC motor used for availability of electrical power
Variable Frequency drive to slowly bring frame holder to extraction speed

## Slide 17: Human Interface Device

## Slide 18: Human Interface Device
2 x 16 segment outdoor LCD display
Reads sensor data
Buttons and switches
Used to turn on and off device
Selects various operating modes
Select what is displayed on LCD

## Slide 19: Microcontroller

## Slide 20: Microcontroller
PSoC 3
Delta Sig ADC
8-bit 8Msps DAC
Integrated LCD Driver
62 GPIO Pins
1.5 – 5.5 V operating range
Cheap $4.33

## Slide 21: Printed Circuit Board
Integrated 5V supply
Easily connect various components
  Humidity Sensor
  Temperature Sensor
  Bluetooth Module
  LCD Display
  Buttons
  Motor Controller
  Relay connections

## Slide 22: Power Supply

## Slide 23
Power Supply
Standard Wall Outlet 115V @ 60 Hertz
300 mA 12V DC power supply
Component | Voltage | Current | Type
Motor | 115V | 3A | AC
Heating Elements | 115 | 4A | AC
Printed Circuit Board | 12V | 300mA | DC

## Slide 24: Remote Control

## Slide 25: Android Development
Purpose:
  Control the Honey Extractor remotely
Android development
  Eclipse integrated development environment (IDE)
  Minimum API level set to 8 (Android v2.2)
  Target application programming interface (API) level 18 (Android v.4.3)
  Developed on Android v.4.03
  Tested on Android v.4.1.2 and v.4.3 platforms

## Slide 26: Android Development

## Slide 27: Bluetooth
Bluetooth HC-06 Slave module
Inexpensive
Operating range up to 10 m
Power supply 5V 50mA
Bluetooth v.2.0+EDR
Baud rate 9600 bps, 8 data bits, 1 stop bit, no parity bit communication format

## Slide 28: Administrative Content

## Slide 29: Work Distribution
 | Brandon | Dmytro | Kira | Petr
 | EE | EE | CpE | EE
Mechanical |  | X |  | X
Software | X |  | X | 
Power supply | X |  |  | 
Heating System | X | X |  | X
Sensors |  | X |  | 
BlueTooth |  |  | X | 
Motor | X |  |  | X
PCB design | X |  |  | 
Parts integration | X | X |  | X

## Slide 30: Bill of Materials
Part | Cost
Mechanical Parts | $400.00
Humidity Sensor | $14.03
Infrared Temperature Sensor | $19.12
Motor | $59.04
Motor Controller | $85.48
Power Supply | $19.99
Printed Circuit Board | $84.99
Electronics | $120.12
BlueTooth Module | $10.60
Heating Element | $102.72
Valve | $15.00
Total | $887.09

## Slide 31: Acknowledgements
Special thanks to:
  Microflex Inc.
  Robotics Club at UCF
  Sergey Retinskiy
  Petr and Dmytriy Boychev

## Slide 32: Questions?